## Slide 1: The Imperative of Disciplined Parallelism: A Hardware Architect’s Perspective
Sarita Adve, Vikram Adve,
Rob Bocchino, Nicholas Carter, Byn Choi, Ching-Tsun Chou,
Stephen Heumann, Nima Honarmand, Rakesh Komuravelli, Maria Kotsifakou,
Pablo Montesinos, Tatiana Schpeisman, Matthew Sinclair, Robert Smolinski,
Prakalp Srivastava, Hyojin Sung, Adam Welc
University of Illinois at Urbana-Champaign, CMU, Intel, Qualcomm
denovo@cs.illinois.edu

## Slide 2: Silver Bullets for the Energy Crisis?
Parallelism
Specialization, heterogeneity, …
BUT large impact on
  Software
  Hardware
  Hardware-Software Interface

## Slide 3: Multicore Parallelism: Current Practice
Multicore parallelism today: shared-memory
  Complex, power- and performance-inefficient hardware
    Complex directory coherence, unnecessary traffic, ...
  Difficult programming model
    Data races, non-determinism, composability?, testing?
  Mismatched interface between HW and SW, a.k.a memory model
    Can’t specify “what value can read return”
    Data races defy acceptable semantics
Fundamentally broken for hardware & software

## Slide 4: Specialization/Heterogeneity: Current Practice
6 different ISAs
7 different parallelism models
Incompatible
memory systems
A modern smartphone
    CPU, GPU, DSP, Vector Units, Multimedia, Audio-Video accelerators
Even more broken

## Slide 5: Energy Crisis Demands Rethinking HW, SW
How to (co-)design
  Software?
  Hardware?
  HW / SW Interface?
Deterministic Parallel Java (DPJ)
DeNovo
Virtual Instruction Set Computing (VISC)
Focus on (homogeneous) parallelism

## Slide 6: Multicore Parallelism: Current Practice
Multicore parallelism today: shared-memory
  Complex, power- and performance-inefficient hardware
    Complex directory coherence, unnecessary traffic, ...
  Difficult programming model
    Data races, non-determinism, composability?, testing?
  Mismatched interface between HW and SW, a.k.a memory model
    Can’t specify “what value can read return”
    Data races defy acceptable semantics
Fundamentally broken for hardware & software

## Slide 7: Multicore Parallelism: Current Practice
Multicore parallelism today: shared-memory
  Complex, power- and performance-inefficient hardware
    Complex directory coherence, unnecessary traffic, ...
  Difficult programming model
    Data races, non-determinism, composability?, testing?
  Mismatched interface between HW and SW, a.k.a memory model
    Can’t specify “what value can read return”
    Data races defy acceptable semantics
Fundamentally broken for hardware & software
Banish shared memory?

## Slide 8: Multicore Parallelism: Current Practice
Multicore parallelism today: shared-memory
  Complex, power- and performance-inefficient hardware
    Complex directory coherence, unnecessary traffic, ...
  Difficult programming model
    Data races, non-determinism, composability?, testing?
  Mismatched interface between HW and SW, a.k.a memory model
    Can’t specify “what value can read return”
    Data races defy acceptable semantics
Fundamentally broken for hardware & software
Banish wild shared memory!
Need disciplined shared memory!

## Slide 9: What is Shared-Memory?
Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization

## Slide 10: What is Shared-Memory?
Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization

## Slide 11: What is Shared-Memory?
Wild Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization

## Slide 12: What is Shared-Memory?
Wild Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization

## Slide 13: What is Shared-Memory?
Disciplined Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization
Explicit, structured side-effects

## Slide 14: Our Approach
Simple programming model AND
Complexity, performance-, power-scalable hardware
Disciplined Shared Memory
Strong safety properties - Deterministic Parallel Java (DPJ)
No data races, determinism-by-default, safe non-determinism
Simple semantics, safety, and composability
Efficiency: complexity, performance, power - DeNovo
Simplify coherence and consistency
Optimize communication and storage layout
explicit effects +
structured
parallel control

## Slide 15: DeNovo Hardware Project
Rethink memory hierarchy for disciplined software
  Started with Deterministic Parallel Java (DPJ)
  End goal is language-oblivious interface
    LLVM-inspired virtual ISA
Software research strategy
  Started with deterministic codes
  Added safe non-determinism
  Ongoing: other parallel patterns, OS, legacy, …
Hardware research strategy
  Homogeneous on-chip memory system
    coherence, consistency, communication, data layout
  Ongoing: heterogeneous systems and off-chip memory

## Slide 16: DeNovo Hardware Project
Rethink memory hierarchy for disciplined software
  Started with Deterministic Parallel Java (DPJ)
  End goal is language-oblivious interface
    LLVM-inspired virtual ISA
Software research strategy
  Started with deterministic codes
  Added safe non-determinism
  Ongoing: other parallel patterns, OS, legacy, …
Hardware research strategy
  Homogeneous on-chip memory system
    coherence, consistency, communication, data layout
  Similar ideas apply to heterogeneous and off-chip memory

## Slide 17: DeNovo Hardware Project
Rethink memory hierarchy for disciplined software
  Started with Deterministic Parallel Java (DPJ)
  End goal is language-oblivious interface
    LLVM-inspired virtual ISA
Software research strategy
  Started with deterministic codes
  Added safe non-determinism [ASPLOS’13]
  Ongoing: other parallel patterns, OS, legacy, …
Hardware research strategy
  Homogeneous on-chip memory system
    coherence, consistency, communication, data layout
  Similar ideas apply to heterogeneous and off-chip memory

## Slide 18: Current Hardware Limitations
Complexity
  Subtle races and numerous transient states in the protocol
  Hard to verify and extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Bandwidth waste (cache-line based communication)
  Cache pollution (cache-line based allocation)

## Slide 19: Results for Deterministic Codes
Complexity
  No transient states
  Simple to extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Bandwidth waste (cache-line based communication)
  Cache pollution (cache-line based allocation)
Base DeNovo
20X faster to verify vs. MESI

## Slide 20: Results for Deterministic Codes
Complexity
  No transient states
  Simple to extend for optimizations
Storage overhead
  No storage overhead for directory information
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Bandwidth waste (cache-line based communication)
  Cache pollution (cache-line based allocation)
Base DeNovo
20X faster to verify vs. MESI

## Slide 21: Results for Deterministic Codes
Complexity
  No transient states
  Simple to extend for optimizations
Storage overhead
  No storage overhead for directory information
Performance and power inefficiencies
  No invalidation, ack messages
  No indirection through directory
  No false sharing: region based coherence
  Region, not cache-line, communication
  Region, not cache-line, allocation (ongoing)
Up to 79% lower memory stall time
Up to 66% lower traffic
Base DeNovo
20X faster to verify vs. MESI

## Slide 22: Outline
Introduction
DPJ Overview
Base DeNovo Protocol
DeNovo Optimizations
Evaluation
Conclusion and Future Work

## Slide 23: DPJ Overview
Deterministic-by-default parallel language [OOPSLA’09]
  Extension of sequential Java
  Structured parallel control: nested fork-join
  Novel region-based type and effect system
  Speedups close to hand-written Java
  Expressive enough for irregular, dynamic parallelism
Supports
  Disciplined non-determinism [POPL’11]
    Explicit, data race-free, isolated
    Non-deterministic, deterministic code co-exist safely (composable)
  Unanalyzable effects using trusted frameworks [ECOOP’11]
  Unstructured parallelism using tasks w/ effects [PPoPP’13]
Focus here on deterministic codes

## Slide 24: DPJ Overview
Deterministic-by-default parallel language [OOPSLA’09]
  Extension of sequential Java
  Structured parallel control: nested fork-join
  Novel region-based type and effect system
  Speedups close to hand-written Java
  Expressive enough for irregular, dynamic parallelism
Supports
  Disciplined non-determinism [POPL’11]
    Explicit, data race-free, isolated
    Non-deterministic, deterministic code co-exist safely (composable)
  Unanalyzable effects using trusted frameworks [ECOOP’12]
  Unstructured parallelism using tasks w/ effects [PPoPP’13]
Focus here on deterministic codes

## Slide 25: Regions and Effects
Region: a name for set of memory locations
  Assign region to each field, array cell
Effect: read or write on a region
  Summarize effects of method bodies
Compiler: simple type check
  Region types consistent
  Effect summaries correct
  Parallel tasks don’t interfere
heap
ST
ST
ST
ST
LD
Type-checked programs are guaranteed determinism-by-default

## Slide 26: Example: A Pair Class
class Pair {
region Blue, Red;
int X in Blue;
int Y in Red;
void setX(int x) writes Blue {
  this.X = x;
}
void setY(int y) writes Red {
  this.Y = y;
}
void setXY(int x, int y) writes Blue; writes Red {
  cobegin {
    setX(x); // writes Blue
    setY(y); // writes Red
  }
}
}
Pair |  | 
Pair.Blue | X | 3
Pair.Red | Y | 42
Declaring and using region names
Region names have static scope (one per class)

## Slide 27: Example: A Pair Class
Writing method effect summaries
class Pair {
region Blue, Red;
int X in Blue;
int Y in Red;
void setX(int x) writes Blue {
  this.X = x;
}
void setY(int y) writes Red {
  this.Y = y;
}
void setXY(int x, int y) writes Blue; writes Red {
  cobegin {
    setX(x); // writes Blue
    setY(y); // writes Red
  }
}
}
Pair |  | 
Pair.Blue | X | 3
Pair.Red | Y | 42

## Slide 28: Example: A Pair Class
Expressing parallelism
class Pair {
region Blue, Red;
int X in Blue;
int Y in Red;
void setX(int x) writes Blue {
  this.X = x;
}
void setY(int y) writes Red {
  this.Y = y;
}
void setXY(int x, int y) writes Blue; writes Red {
  cobegin {
    setX(x);
    setY(y);
  }
}
}
Pair |  | 
Pair.Blue | X | 3
Pair.Red | Y | 42

## Slide 29: Example: A Pair Class
Expressing parallelism
class Pair {
region Blue, Red;
int X in Blue;
int Y in Red;
void setX(int x) writes Blue {
  this.X = x;
}
void setY(int y) writes Red {
  this.Y = y;
}
void setXY(int x, int y) writes Blue; writes Red {
  cobegin {
    setX(x); // writes Blue
    setY(y); // writes Red
  }
}
}
Pair |  | 
Pair.Blue | X | 3
Pair.Red | Y | 42
Inferred effects

## Slide 30: Outline
Introduction
Background: DPJ
Base DeNovo Protocol
DeNovo Optimizations
Evaluation
Conclusion and Future Work

## Slide 31: Memory Consistency Model
Guaranteed determinism  Read returns value of last write in sequential order
  Same task in this parallel phase
  Or before this parallel phase
LD 0xa
ST 0xa
Parallel
Phase
ST 0xa
Coherence
Mechanism

## Slide 32: Cache Coherence
Coherence Enforcement
  Invalidate stale copies in caches
  Track one up-to-date copy
Explicit effects
  Compiler knows all regions written in this parallel phase
  Cache can self-invalidate before next parallel phase
    Invalidates data in writeable regions not accessed by itself
Registration
  Directory keeps track of one up-to-date copy
  Writer updates before next parallel phase

## Slide 33: Basic DeNovo Coherence [PACT’11]
Assume (for now): Private L1, shared L2; single word line
  Data-race freedom at word granularity
L2 data arrays double as directory
  Keep valid data or registered core id, no space overhead
L1/L2 states
Touched bit set only if read in the phase
registry
Invalid
Valid
Registered
Read
Write
Write

## Slide 34: Example Run
R | X0 | V | Y0
R | X1 | V | Y1
R | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
class S_type {
X in DeNovo-region ;
Y in DeNovo-region ;
}
S _type S[size];
...
Phase1 writes { // DeNovo effect
foreach i in 0, size {
S[i].X = …;
}
self_invalidate( );
}
L1 of Core 1
R | X0 | V | Y0
R | X1 | V | Y1
R | X2 | V | Y2
I | X3 | V | Y3
I | X4 | V | Y4
I | X5 | V | Y5
L1 of Core 2
I | X0 | V | Y0
I | X1 | V | Y1
I | X2 | V | Y2
R | X3 | V | Y3
R | X4 | V | Y4
R | X5 | V | Y5
Shared L2
R | C1 | V | Y0
R | C1 | V | Y1
R | C1 | V | Y2
R | C2 | V | Y3
R | C2 | V | Y4
R | C2 | V | Y5
R = Registered
V = Valid
I = Invalid
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
R | X3 | V | Y3
R | X4 | V | Y4
R | X5 | V | Y5
Registration
Registration
Ack
Ack

## Slide 35: Practical DeNovo Coherence
Basic protocol impractical
  High tag storage overhead (a tag per word)
Address/Transfer granularity > Coherence granularity
DeNovo Line-based protocol
  Traditional software-oblivious spatial locality
  Coherence granularity still at word
    no word-level false-sharing
“Line Merging”
Cache
 |  | V |  |  | V | R | 
Tag
V | V |  |  |  |  |  | V

## Slide 36: Current Hardware Limitations
Complexity
  Subtle races and numerous transient sates in the protocol
  Hard to extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Traffic (cache-line based communication)
  Cache pollution (cache-line based allocation)
✔
✔
✔
✔

## Slide 37: Flexible, Direct Communication
Insights
  1. Traditional directory must be updated at every transfer
  DeNovo can copy valid data around freely
  2. Traditional systems send cache line at a time
  DeNovo uses regions to transfer only relevant data
  Effect of AoS-to-SoA transformation w/o programmer/compiler

## Slide 38: Flexible, Direct Communication
L1 of Core 1
…
…
R | X0 | V | Y0 | V | Z0
R | X1 | V | Y1 | V | Z1
R | X2 | V | Y2 | V | Z2
I | X3 | V | Y3 | V | Z3
I | X4 | V | Y4 | V | Z4
I | X5 | V | Y5 | V | Z5
L1 of Core 2
…
…
I | X0 | V | Y0 | V | Z0
I | X1 | V | Y1 | V | Z1
I | X2 | V | Y2 | V | Z2
R | X3 | V | Y3 | V | Z3
R | X4 | V | Y4 | V | Z4
R | X5 | V | Y5 | V | Z5
Shared L2
…
…
R | C1 | V | Y0 | V | Z0
R | C1 | V | Y1 | V | Z1
R | C1 | V | Y2 | V | Z2
R | C2 | V | Y3 | V | Z3
R | C2 | V | Y4 | V | Z4
R | C2 | V | Y5 | V | Z5
Registered
Valid
Invalid
X3
LD X3
Y3
Z3

## Slide 39: Flexible, Direct Communication
L1 of Core 1
…
…
R | X0 | V | Y0 | V | Z0
R | X1 | V | Y1 | V | Z1
R | X2 | V | Y2 | V | Z2
I | X3 | V | Y3 | V | Z3
I | X4 | V | Y4 | V | Z4
I | X5 | V | Y5 | V | Z5
L1 of Core 2
…
…
I | X0 | V | Y0 | V | Z0
I | X1 | V | Y1 | V | Z1
I | X2 | V | Y2 | V | Z2
R | X3 | V | Y3 | V | Z3
R | X4 | V | Y4 | V | Z4
R | X5 | V | Y5 | V | Z5
Shared L2
…
…
R | C1 | V | Y0 | V | Z0
R | C1 | V | Y1 | V | Z1
R | C1 | V | Y2 | V | Z2
R | C2 | V | Y3 | V | Z3
R | C2 | V | Y4 | V | Z4
R | C2 | V | Y5 | V | Z5
Registered
Valid
Invalid
X3
X4
X5
R | X0 | V | Y0 | V | Z0
R | X1 | V | Y1 | V | Z1
R | X2 | V | Y2 | V | Z2
V | X3 | V | Y3 | V | Z3
V | X4 | V | Y4 | V | Z4
V | X5 | V | Y5 | V | Z5
LD X3
Flexible, Direct Communication

## Slide 40: Current Hardware Limitations
Complexity
  Subtle races and numerous transient sates in the protocol
  Hard to extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Traffic (cache-line based communication)
  Cache pollution (cache-line based allocation)
✔
✔
✔
✔
✔
✔
✔
ongoing

## Slide 41: Outline
Introduction
Background: DPJ
Base DeNovo Protocol
DeNovo Optimizations
Evaluation
  Complexity
  Performance
Conclusion and Future Work

## Slide 42: Protocol Verification
DeNovo vs. MESI word with Murphi model checking
Correctness
  Six bugs in MESI protocol
    Difficult to find and fix
  Three bugs in DeNovo protocol
    Simple to fix
Complexity
  15x fewer reachable states for DeNovo
  20x difference in the runtime

## Slide 43: Performance Evaluation Methodology
Simulator: Simics + GEMS + Garnet
System Parameters
  64 cores
  Simple in-order core model
Workloads
  FFT, LU, Barnes-Hut, and radix from SPLASH-2
  bodytrack and fluidanimate from PARSEC 2.1
  kd-Tree (two versions) [HPG 09]

## Slide 44
FFT
LU
kdFalse
kdPadded
Barnes
bodytrack
Chart: 
| MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF
L1 STALL | 0.3192 | 0.1864 | 0.0204 | 0.0068
L2 Hit | 5.4945 | 5.5306 | 8.3414 | 8.2534
R L1 Hit | 0.2964 | 0.3214 | 0.6844 | 0.9541
Mem Hit | 0.3292 | 0.332 | 6.0767 | 5.8712
fluidanimate
radix
Chart: Memory Stall Time
| MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF
L1 STALL | 0.0641 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
L2 Hit | 0.3386 | 1.1589 | 1.7049 | 1.5638 | 1.7845 | 1.2942 | 0.4929 | 0.4188 | 2.1154 | 2.1133 | 0.4649 | 0.2781
R L1 Hit | 3.7451 | 2.4864 | 0.025 | 0.1951 | 0.1777 | 0.7803 | 0.0356 | 0.1389 | 0.0739 | 0.0701 | 0.2419 | 0.425
Mem Hit | 0.0152 | 0.0177 | 0.0002 | 0.0002 | 0 | 0 | 0.0819 | 0.0851 | 0.3301 | 0.3427 | 0.1689 | 0.1769
DW’s performance competitive with MW
MESI Word (MW) vs. DeNovo Word (DW)

## Slide 45
FFT
LU
kdFalse
kdPadded
Barnes
bodytrack
Chart: 
| MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF
L1 STALL | 0.3192 | 0.1864 | 0.0068 | 0.0961 | 0.0204 | 0.0068 | 0 | 0.0007
L2 Hit | 5.4945 | 5.5306 | 0.8126 | 0.7947 | 8.3414 | 8.2534 | 0.5644 | 0.5935
R L1 Hit | 0.2964 | 0.3214 | 0.0724 | 0.0437 | 0.6844 | 0.9541 | 0.0618 | 0.0797
Mem Hit | 0.3292 | 0.332 | 0.1082 | 0.1111 | 6.0767 | 5.8712 | 0.3738 | 0.3501
fluidanimate
radix
Chart: Memory Stall Time
| MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF | MW | DW | ML | DL | DDF
L1 STALL | 0.0641 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
L2 Hit | 0.3386 | 1.1589 | 0.5038 | 0.337 | 1.7049 | 1.5638 | 0.4226 | 0.3406 | 1.7845 | 1.2942 | 0.8039 | 0.815 | 0.4929 | 0.4188 | 0.736 | 0.2345 | 2.1154 | 2.1133 | 0.9051 | 0.9064 | 0.4649 | 0.2781 | 0.9652 | 0.9948
R L1 Hit | 3.7451 | 2.4864 | 0.491 | 0.6038 | 0.025 | 0.1951 | 0.5773 | 0.0379 | 0.1777 | 0.7803 | 0.1961 | 0.1961 | 0.0356 | 0.1389 | 0.264 | 0.0083 | 0.0739 | 0.0701 | 0.0938 | 0.0181 | 0.2419 | 0.425 | 0.0231 | 0.0365
Mem Hit | 0.0152 | 0.0177 | 0.0052 | 0.0062 | 0.0002 | 0.0002 | 0.0001 | 0.0001 | 0 | 0 | 0 | 0 | 0.0819 | 0.0851 | 0 | 0 | 0.3301 | 0.3427 | 0.001 | 0.0014 | 0.1689 | 0.1769 | 0.0116 | 0.0126
DL about the same or better memory stall time than ML
DL outperforms ML significantly with apps with false sharing
MESI Line (ML) vs. DeNovo Line (DL)

## Slide 46
FFT
LU
kdFalse
kdPadded
Barnes
bodytrack
fluidanimate
radix
Chart: 
| ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF
L1 STALL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0068 | 0.0961 | 0.0927 | 0 | 0.0007 | 0.0006
L2 Hit | 0.5038 | 0.337 | 0.2095 | 0.4226 | 0.3406 | 0.4153 | 0.8039 | 0.815 | 0.8232 | 0.736 | 0.2345 | 0.2123 | 0.9051 | 0.9064 | 0.8086 | 0.9652 | 0.9948 | 1.0205 | 0.8126 | 0.7947 | 0.8026 | 0.5644 | 0.5935 | 0.5918
R L1 Hit | 0.491 | 0.6038 | 0.2022 | 0.5773 | 0.0379 | 0.0077 | 0.1961 | 0.1961 | 0.0845 | 0.264 | 0.0083 | 0.0009 | 0.0938 | 0.0181 | 0.0023 | 0.0231 | 0.0365 | 0.0204 | 0.0724 | 0.0437 | 0.0141 | 0.0618 | 0.0797 | 0.0459
Mem Hit | 0.0052 | 0.0062 | 0.0062 | 0.0001 | 0.0001 | 0.0001 | 0 | 0 | 0 | 0 | 0 | 0 | 0.001 | 0.0014 | 0.0014 | 0.0116 | 0.0126 | 0.0126 | 0.1082 | 0.1111 | 0.1102 | 0.3738 | 0.3501 | 0.3474
 | 100 | 94.7 | 41.79 | 100 | 37.86 | 42.31 | 100 | 101.11 | 90.77 | 100 | 24.28 | 21.32 | 99.99 | 92.59 | 81.23 | 99.99 | 104.39 | 105.35 | 100 | 104.56 | 101.96 | 100 | 102.4 | 98.57
Combined optimizations perform best
  Except for LU and bodytrack
  Apps with low spatial locality suffer from line-granularity allocation
Optimizations on DeNovo Line

## Slide 47
Chart: 
| ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF
Read | 0.6551 | 0.3996 | 0.2075 | 0.6033 | 0.2841 | 0.2673 | 0.7136 | 0.6903 | 0.6194 | 0.7054 | 0.4553 | 0.406 | 0.7537 | 0.7444 | 0.6078 | 0.8063 | 0.7789 | 0.7929 | 0.5659 | 0.3755 | 0.3749 | 0.6394 | 0.4112 | 0.4035
Write | 0.136 | 0.4269 | 0.4269 | 0.1245 | 0.2537 | 0.2548 | 0.0799 | 0.1589 | 0.159 | 0.0982 | 0.0178 | 0.0178 | 0.0483 | 0.0303 | 0.0305 | 0.0193 | 0.1442 | 0.1439 | 0.0664 | 0.8897 | 0.894 | 0.0592 | 0.8455 | 0.8455
WB | 0.0325 | 0.0232 | 0.0231 | 0.1031 | 0.1155 | 0.112 | 0.034 | 0.0661 | 0.0639 | 0.0213 | 0.0188 | 0.0179 | 0.0355 | 0.0322 | 0.0341 | 0.032 | 0.033 | 0.033 | 0.2558 | 0.2434 | 0.2455 | 0.1941 | 0.2304 | 0.2295
Invalidation | 0.1765 | 0 | 0 | 0.1691 | 0 | 0 | 0.1724 | 0 | 0 | 0.1751 | 0 | 0 | 0.1625 | 0 | 0 | 0.1425 | 0 | 0 | 0.1119 | 0 | 0 | 0.1073 | 0 | 0
DeNovo has less traffic than MESI in most cases
DeNovo incurs more write traffic
  due to word-granularity registration
  Can be mitigated with “write-combining” optimization
FFT
LU
kdFalse
kdPadded
Barnes
bodytrack
fluidanimate
radix
Network Traffic

## Slide 48
Chart: 
| ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF | ML | DL | DDF
Read | 0.6551 | 0.3996 | 0.2075 | 0.6033 | 0.2841 | 0.2673 | 0.7136 | 0.6903 | 0.6194 | 0.7054 | 0.4553 | 0.406 | 0.7537 | 0.7444 | 0.6078 | 0.8063 | 0.7789 | 0.7929 | 0.5659 | 0.3755 | 0 | 0.6394 | 0.4112 | 0
Write | 0.136 | 0.4269 | 0.4269 | 0.1245 | 0.2537 | 0.2548 | 0.0799 | 0.1589 | 0.159 | 0.0982 | 0.0178 | 0.0178 | 0.0483 | 0.0303 | 0.0305 | 0.0193 | 0.1442 | 0.1439 | 0.0664 | 0.1 | 0 | 0.0592 | 0.3491 | 0
WB | 0.0325 | 0.0232 | 0.0231 | 0.1031 | 0.1155 | 0.112 | 0.034 | 0.0661 | 0.0639 | 0.0213 | 0.0188 | 0.0179 | 0.0355 | 0.0322 | 0.0341 | 0.032 | 0.033 | 0.033 | 0.2558 | 0.2434 | 0 | 0.1941 | 0.2304 | 0
Invalidation | 0.1765 | 0 | 0 | 0.1691 | 0 | 0 | 0.1724 | 0 | 0 | 0.1751 | 0 | 0 | 0.1625 | 0 | 0 | 0.1425 | 0 | 0 | 0.1119 | 0 | 0 | 0.1073 | 0 | 0
DeNovo has less or comparable traffic than MESI
Write combining effective
FFT
LU
kdFalse
kdPadded
Barnes
bodytrack
fluidanimate
radix
Network Traffic

## Slide 49: L1 Fetch Bandwidth Waste
Most data brought into L1 is wasted
  40—89% of MESI data fetched is unnecessary
  DeNovo+Flex reduces traffic by up to 66%
  Can we also reduce allocation waste?
Chart: Normalized Bandwidth Waste
| MESI | DeNovo | DeNovo+Flex | MESI | DeNovo | DeNovo+Flex | ParKD | Fluidanimate
Used | 0.22244 | 0.2223 | 0.2223 | 0.38638 | 0.38614 | 0.38615
Waste | 0.62073 | 0.62561 | 0.30196 | 0.60795 | 0.32259 | 0.32261
Unknown | 0.15682 | 0.036062 | 0.020623 | 0.0056679 | 0.0001315 | 0.00013215
Region-driven data layout

## Slide 50: Current Hardware Limitations
Complexity
  Subtle races and numerous transient sates in the protocol
  Hard to extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Traffic (cache-line based communication)
  Cache pollution (cache-line based allocation)
✔
✔
✔
✔
✔
✔
✔
ongoing

## Slide 51: Current Hardware Limitations
Complexity
  Subtle races and numerous transient sates in the protocol
  Hard to extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Traffic (cache-line based communication)
  Cache pollution (cache-line based allocation)
✔
✔
✔
✔
✔
✔
✔
ongoing
Region-Driven Memory Hieararchy

## Slide 52: Conclusions and Future Work (1 of 2)
Simple programming model AND
Complexity, performance-, power-scalable hardware
Disciplined Shared Memory
Strong safety properties - Deterministic Parallel Java (DPJ)
No data races, determinism-by-default, safe non-determinism
Simple semantics, safety, and composability
Efficiency: complexity, performance, power - DeNovo
Simplify coherence and consistency
Optimize communication and storage layout
explicit effects +
structured
parallel control

## Slide 53: Conclusions and Future Work (2 of 2)
DeNovo rethinks hardware for disciplined models
For deterministic codes
Complexity
  No transient states: 20X faster to verify than MESI
  Extensible: optimizations without new states
Storage overhead
  No directory overhead
Performance and power inefficiencies
  No invalidations, acks, false sharing, indirection
  Flexible, not cache-line, communication
  Up to 79% lower memory stall time, up to 66% lower traffic
ASPLOS’13 paper adds safe non-determinism

## Slide 54: Conclusions and Future Work (3 of 3)
Broaden software supported
  Pipeline parallelism, OS, legacy, …
Region-driven memory hierarchy
  Also apply to heterogeneous memory
    Global address space
    Region-driven coherence, communication, layout
Hardware/Software Interface
  Language-neutral virtual ISA
Parallelism and specialization may solve energy crisis, but
  Require rethinking software, hardware, interface
  The Disciplined Parallel Programming Imperative